## Slide 1
Performance of the ATLAS RPC detector and trigger at 13 TeV
Heng Li (University of Science and Technology of China) on behalf of the ATLAS Collaboration
The ATLAS RPC Detector and Trigger System
Trigger timing performance
Detector efficiency overall performance
Trigger efficiency vs. offline muon η/φ
Introduction
The ATLAS experiment utilises the Resistive Plate Chambers detector (RPC) for the first level muon trigger system in the barrel region of the detector. This poster presents measurements of RPC detector and trigger performance using proton-proton collisions at a centre-of-mass energy of 13 TeV collected in 2018, showing results in terms of the trigger timing and efficiency.
The present ATLAS muon trigger in the barrel region based on
3 concentric RPC layers
16 physical sectors, more than 3700 gas volumes
each physical sector is segmented in 2 trigger sectors
totally 64 trigger sectors in side A and side C
each trigger sector is segmented along η in towers
Plateau value of the trigger efficiency as a function of time [2].
each point corresponds to a different ATLAS run recorded in 2017
only runs with integrated luminosity greater than 50 pb-1 and at least 1000 muons collected are used
The Level-1 (L1) trigger algorithm is based on hit coincidence of 3 concentric RPC stations
Low pT trigger: coincidence between the innermost two RPC stations
High pT trigger: additional confirmation on the third external station
Fraction of RPC trigger hits associated to the correct BC [1] for each of the barrel muon trigger towers for one example run in 2017 [2].
Fraction for the whole RPC trigger system as a function of time. Each point corresponds to a different ATLAS run recorded in 2017 [2]. The fraction of high pT muons associated to the correct BC is 99.6% [1].
L1 muon barrel trigger efficiency for reconstructed muons as a function of transverse momentum is shown for 6 L1 thresholds [2].
efficiencies for the low pT trigger thresholds (MU4, MU6, MU10) reach a plateau of about 80%
efficiencies for high pT trigger thresholds (MU11, MU20, MU21) rise to around 70% [1]
Trigger efficiency vs. offline muon pT
Performance in one detector volume
[1] M. Corradi, Performance of ATLAS RPC Level-1 muon trigger during the 2015 data taking, 6032 Journal of Instrumentation 11 (2016) C09003
[2] ATLAS Collaboration, ATL-COM-DAQ-2018-008
Fit per run